## Slide 1
CNN-based Deep Learning-Enabled Tool for Winter Roadway Condition Monitoring
Yong Lee¹, Mingjian Wu², Tae J. Kwon³
¹Dean’s Research Awards Student, ²Graduate Research Assistant, ³Asscoiate Professor
¹Department of Electrical and Computer Engineering & ²,³Department of Civil and Environmental Engineering, University of Alberta, Edmonton, AB, Canada, T6G 2W2
Introduction & Background
Methodology
Work Zone
Objectives
Introduction ​​
Winter challenges road safety and mobility with snow and ice, necessitating effective maintenance strategies. While Road Weather Information Systems (RWIS) equipped with cameras have improved the monitoring of road conditions, the manual analysis of Road Surface Conditions (RSC) captured by these cameras is still time-inefficient and labour-intensive.
Background ​ ​​
Advances in artificial intelligence and computer vision allow for the automated monitoring of RSC through RWIS image analysis. This enables real-time monitoring and reduces labor costs, which are vital for improving road safety and efficiency during winter.
Highway
Residential
Study Area & Data Collection ​
Conclusions
A CNN-based deep learning model was developed to automate RSC recognition from stationary RWIS images, demonstrating high accuracy in training and validation. Its success not only proves its precision in identifying RSC but also showcases its potential in advancing towards a pseudo-real-time road condition monitoring system, offering significant cost and labor reductions in road safety operations.
Results
Acknowledgement
RWIS Database:
Camera Data
Traffic Data
Atmospheric Data
Surface Data
Convolution
Input
Feature Extraction
Classification
Pooling
Output
Fully Connected
Stationary RWIS
Dec 2022 – Feb 2023
Iowa RWIS Location
Image Labelling ​
Training & Testing with Convolutional Neural Networks (CNN) ​
Performance Evaluation and Results Analysis ​
Comparison of Unbalanced and Balanced Image Datasets ​
Grad-CAM: Visual Explanations via Gradient-based Localization ​
Chart: 10-year Average Snow (cm) in Iowa by Month
| January | February | March | April | May | October | November | December
 | 21.9 | 35.3 | 9.8 | 1 | 1.8 | 0.6 | 5.7 | 16.6
Snowy
Road
Bare
Road
Grad-CAM enhances CNN interpretability by highlighting image regions most influential in classification, such as snow or bare pavement, offering insights into model decisions and improvement areas.
Unbalanced 7,164 Images (7.2k)
67 Individual Angles
Balanced 2,200 Images (2.2k)
17 Individual Angles
Chart: Distribution of Road Surface Conditions for 7.2k
| Bare Road | Snowy Road
 | 5447 | 1717
Chart: Distribution of Road Surface Conditions For 2.2k
| Bare Road | Snowy Road
 | 1148 | 1061
The authors extend their gratitude to the Faculty of Engineering for the support provided through the Dean’s Research Awards Program. This program has been crucial in facilitating this study by providing a platform and the necessary opportunities for research. Additionally, the authors wish to acknowledge the Iowa Department of Transportation for supplying the essential datasets necessary for our research.
21% of All Vehicle Crashes are
Weather-related in U.S.
Winter Maintenance Annual Cost In U.S.
Direct $2.3B Indirect $5B
Winter Traffic Mobility Capacity 44%↓
Speed 17%↓
Chart: Accuracy Score and F1 Score (Binary) Comparison of Two Dataset
| F1 Score | Accuracy
7.2k | 0.9719 | 0.9867
2.2k | 0.9369 | 0.9412
​The objective is to improve winter road monitoring with Convolutional Neural Networks (CNN) to enable near real-time RSC monitoring by interpolating between RWIS points.
Snowy
Snowy
Bare
Bare
Snowy
Bare
……..